## Slide 1: Low-Pass Filter
Derek Weitzel
Yutaka Tsutano

## Slide 2: Introduction
Design a Low-Pass Filter using synthesized components.
Optimize design for power at the algorithmic level.
Test the Low-Pass filter with a functional verification version.

## Slide 3: Finite Impulse Filter (FIR)
Weighted sum of the most recent N samples:
Convolution
Notes: Yutaka

## Slide 4: Filter Design
Designed using Matlab
Filter Properties
  Finite Impulse Low-Pass Filter w/ Hamming Window
  Sampling Freq: 8194 Hz
  Cut-off Freq: 2048 Hz
Notes: Yutaka

## Slide 5: Fixed-Point Number Format “Q15”
Standard arithmetic hardware can be used
    Floating-point unit is expensive
Q15 number has 15 fractional bits
Notes: Yutaka

## Slide 6: VHDL Simulation
ModelSim
Functional simulator was developed in C++ to generate test cases
Produced same output
VHDL Test Bench
C++

## Slide 7: Optimization
Typical FIR filter is symmetric
Naive
Optimized
Notes: Yutaka

## Slide 8: Optimization
Removed 3 Multipliers
Replaced with optimized Adders.
  Ripple-Carry adders for power optimization.
Reduced clock frequency to reduce transitions.

## Slide 9: Convolution Hardware
Area = 5024508 micron2
3220 stdCells
Encounter routing introduced DRC errors.
Clearly see the four multipliers.

## Slide 10: Datapath

## Slide 11: Final Chip
2500 x 2500 micron chip
Routing introduced DRC errors.
Registers on right. Adders on top.
Input on right. Output on top.

## Slide 12: Conclusions
Majority of time spent working in Cadence.
LVS difficult for synthesized systems, eg. Final Layout. Requires extracted layouts of all components.
Low-Pass filter completed!